## Slide 1: Computer Architecture: Memory Safety & Protection
Dr. Colin O’Flynn

## Slide 2: Lectures
How does a program run on a machine?
How do you compile from high-level code to machine code?
How does the machine run? (Control Flow)
How does the machine store data?
How does the machine interface using buses?
What does it mean to have “allowed” memory?
How does the machine speed up data access?

## Slide 3: Busses that don’t respond or Invalid
Prior lecture looked at busses
This lecture will go beyond just “non-existent”

## Slide 4: Memory Safety
Memory safety helps:
  Protect against unintended natural events (bit-flips)
  Protect against bugs that could cause dangerous operations
  Protect against attackers exploiting the memory features

## Slide 5: Memory Error Correction (ECC)
In 2003, a candidate in a Belgium election received 4096 extra votes… a suspicious number…

## Slide 6: ECC Memory
Extra bits used to store data to determine if there is an error.
Can sometimes recover from a single bit-flip.
Question of how many bits to use in ECC vs. memory, as impacts efficiency.

## Slide 7: ECC Memory in Servers
Not just embedded systems – “server-grade” memory often has ECC.
Detects & can fix a certain number of bit flips.

## Slide 8: Microcontroller ECC Memory
Certain memory types (FLASH memory) often contain ECC as they degrade with use. This will be (normally) hidden from you.
ECC memory in microcontroller RAM is relatively rare for general use.
Microcontrollers designed for safety-critical use (automotive) very likely to include these features.

## Slide 9: Invalid Memory Access Problems
Memory corruption is one problem, but what about:
  Microcontroller tries to write somewhere invalid?
  Microcontroller tries to execute from an area that isn’t actually code?

## Slide 10: e.g., HeartBleed
https://commons.wikimedia.org/wiki/File:Heartbleed_bug_explained.svg

## Slide 11: e.g., HeartBleed
https://commons.wikimedia.org/wiki/File:Heartbleed_bug_explained.svg

## Slide 12: Memory Overwriting & Reading
Lots of examples of this in practice – but in general an attacker tries to write to or read from memory they should not be allowed to access.
Often an attacker wants to execute some buffer they have written a program to.

## Slide 13: Hardware Memory Protection
Ideally each task would only have access to certain data.
The capabilities of the MPU depend on the device.
Minimum supports at least two modes

## Slide 14: Privileged & Unprivileged Modes

## Slide 15: Read / Write / Execute Permissions
Similar to on e.g., Linux:
  Files can have permission for “read”, “write” and “execute”
  Permissions can vary for owner or others (e.g., privileged vs. unprivileged)
MPUs enforce this over address spaces.
You need to carefully manage your address spaces to help with this.

## Slide 16: Note: Harvard Architecture
Harvard architectures naturally enforce non-execute on data
  Impossible in all cases to execute from the data region!
Arm by default allow execution from data region (even if you never use it).

## Slide 17: Memory Access Logic
CPU Address
Access Regions
Address Relocation
Physical Memory
+
Check
FAIL: Trap

## Slide 18: Address Space Layout Randomization (ASLR)
Now common on Oses (not microcontrollers) – randomly changes where processes are in memory
Makes it difficult (impossible) for attacker to exploit normal orders

## Slide 19: MPU & MMU
MPU (Memory Protection Unit)
  Normally part of microcontrollers
  Fixed number of regions we can configure
MMU (Memory Management Unit)
  Normally part of “application-class” processors (e.g., Running Linux/Android/Oses)
  Address virtualization support, many additional features

## Slide 20: MPU Example
Note MPU is part of the core
DMA (another bus controller) is not bound by MPU!

## Slide 21: STM32F3 MPU Setup
E.g., disable execution from RAM

## Slide 22: STM32 MPU Introduction
https://www.st.com/resource/en/application_note/an4838-introduction-to-memory-protection-unit-management-on-stm32-mcus-stmicroelectronics.pdf
https://www.st.com/resource/en/programming_manual/pm0214-stm32-cortexm4-mcus-and-mpus-programming-manual-stmicroelectronics.pdf

## Slide 23: STM32 MPU Demo
<See Segger>

## Slide 24: Memory Safe Languages
C is not memory safe as you can do this:
char buffer[8];
buffer[8] = ‘x’;
You may get a compiler warning in that case, but if passed as a pointer there would be no warning.
This is the exact bug type that caused the HeartBleed attack earlier.

## Slide 25: More Invalid C Demos

## Slide 26: Memory Safe Languages
Hardware cannot prevent many of these problems – MPU would see them as valid.
Memory-safe language guarantees:
  No buffer overflow
  No use-after-free
  No dangling pointers
  No invalid pointer arithmetic

## Slide 27: Memory Unsafe Language Hints
Generally memory-unsafe languages allow you to:
  Directly manipulate pointers
  Cast any value to any other value
  Perform manual memory management

## Slide 28: Memory Safe Languages
Language | Approach
Java | Runtime checks
Python | Runtime checks
Go | Garbage collection
Rust | Compile-time safety
Swift | Strong type system
E.g., a few languages & how they achieve that goal:

## Slide 29: Runtime Memory Safety
Enforced at runtime – not detected until you try and execute the code:
Bounds checking
Null checks
Garbage collection
Type Safety

## Slide 30: Compiler-Time Memory Safety
Rust prevents errors before execution
Perfect for embedded systems where can be difficult to see error lots.
Concepts of this mean tracking:
  Ownership
  Borrowing
  Lifetimes

## Slide 31: Rust Ownership Model
Every value was one owner.
Ownership can move.
References must following borrowing rules.
Lifetimes are checked and must be valid.
See next page for example

## Slide 32: e.g., Rust compiling an error
https://play.rust-lang.org/?version=stable&mode=debug&edition=2024

## Slide 33: Memory Safe CPU Architectures
New designs of processors try to enforce some of these concepts in hardware.
Capability Hardware Enhanced RISC Instructions (CHERI) and CHERIoT are two variants of this idea (higher & lower performance)
In CHERI pointers become capabilities:
  Capabilities in hardware track address, bounds, permissions, and validity

## Slide 34: CPU Core: Initial

## Slide 35: CPU Core: Initial

## Slide 36: e.g., CHERIoT Code (Programmer View)
https://github.com/CHERIoT-Platform/cheriot-rtos/blob/main/examples/08.memory_safety/memory_safety_inner.cc#L69

## Slide 37: Other Features: Capabilities and Compartments

## Slide 38: Hardware Enforced Memory Safety
Unlike with programming language, the code will not run.
Trade-off as may want to determine this at compile-time when that could be know.
  Analysis tools can also determine this, leading to “best of both worlds”
CHERIoT is new – first physical devices demonstrated this year, but active development
May be something you run across later in your career!

## Slide 39: Memory Safety Summary
Memory safety normally refers to preventing “out of bounds” access.
Often presents a security risk, but also a safety risk if e.g., crashing program causes a physical device to misbehave.
Memory Protection Unit (MPU) is most commonly used device in smaller microcontrollers to enforce region level access.
Memory-safe languages (such as Rust) and architectures (such as CHERIoT) gaining wider acceptance in embedded.