## Slide 1: Computer Architecture: Pipelines
Dr. Colin O’Flynn

## Slide 2: Lectures
How does a program run on a machine?
How do you compile from high-level code to machine code?
How does the machine run? (Control Flow)
How does the machine store, access, and control data?
How does the machine execute instructions?
How is execution made more efficient?
How do we measure execution?

## Slide 3: Pipeline Context

## Slide 4: RISC-V Instruction Set

## Slide 5: A Simple RISC-V Program
int AddAndMul(int a, int b){
int c;
c = a + b;
c = c * a;
c = c * b;
return c;
}
AddAndMul(int, int):
add a5,a0,a1
mul a0,a5,a0
mul a0,a1,a0
ret
0x00b507b3
0x2a78533
0x2a58533
0x8082
C (High Level)
ASM (Lower Level)
Binary / Machine
Compiler
Assembler
NOTE: in RISC-V a0/a1/etc are general-purpose registers.

## Slide 6: Executing a Simple Program (Naïve)
  0x00b507b3
  0x2a78533
  0x2a58533
  0x8082
Storage Media
Decode Logic
ALU
add a5,a0,a1
a
  0x00b507b3
a0
a1
b
c
a5
PC
+
a5 = a0 + a1

## Slide 7: e.g., interactive simulation
https://eseo-tech.github.io/emulsiV/
add x15, x10, x11
add x10, x15, x10
add x10, x11, x10
jalr x1, x0, 0

## Slide 8: About Logic Propagation Time

## Slide 9: Simple Pipeline Example
  0x00b507b3
  0x2a78533
  0x2a58533
  0x8082
Storage Media
Fetch
Decode
Execute
0x00b507b3
add a5,a0,a1
a5 = a0 + a1
0x2a78533
mul a0,a5,a0
0x2a58533
a0 = a5 × a0
mul a0,a1,a0
0x8082
Clock Cycle: 1 2 3 4
Time
NOTE: in RISC-V a0/a1/etc are general-purpose registers.

## Slide 10: Human Pipelining Examples
You probably already “pipeline” lots of tasks, e.g.:
Doing laundry
Cooking / Baking
Making instant noodles
Fill and Turn On Kettle
Open Ramen & Packets / Grab Utensils
Pour Water
Wait
Eat

## Slide 11: 2 vs 3 vs 5 vs … stage pipeline
Frontend
Backend
(1) Instruction Fetch & Decode
(2) Execute & Writeback
(1) Instruction Fetch (2) Decode
(3) Execute & Writeback
(1) Instruction Fetch (2) Decode
(3) Execute (4) Writeback
(1) Instruction Fetch (2) Decode
(3) Execute (4) Memory (5) Register Writeback
Plans the code the backend will execute. Goal is to keep the backend busy as much as possible.
Actually executes the instructions, including writing anything to memory or registers.

## Slide 12: Substages within Stages
Pentium 4 had 20 stage pipeline(2000). A later version (P4E, 2004) went up to 31. Things have calmed down since then.
Intel Atom (2008)

## Slide 13: Pipeline Hazards
Control hazard
  Need result of a conditional (branch?) before conditional result is ready
Structural hazard
  Need the same resource (e.g., multiplier hardware)
Data hazard
  Instruction to execute needs result of not-finished instruction

## Slide 14: What Hazards are Here?
Fetch
Decode
Execute
0x00b507b3
add a5,a0,a1
a5 = a0 + a1
0x2a78533
mul a0,a5,a0
0x2a58533
a0 = a5 × a0
mul a0,a1,a0
0x8082
Clock Cycle: 1 2 3 4
Time

## Slide 15: Remember – Logic can be SLOW

## Slide 16: Example – NEORV32 Multiply Timing
https://stnolting.github.io/neorv32/

## Slide 17: Example: 2-Cycle Multiply
a0 = a5 × a0
Fetch
Decode
Execute
0x00b507b3
add a5,a0,a1
a5 = a0 + a1
0x2a78533
mul a0,a5,a0
0x2a58533
mul a0,a1,a0
0x8082
Clock Cycle: 1 2 3 4 5
Time
a0 = a5 × a0
ret
Here is BOTH a structural hazard & a data hazard (if we had another multiplier)

## Slide 18: Example: 2-Cycle Multiply
Fetch
Decode
Execute
mul a0,a1,a0
0x8082
Clock Cycle: 4 5 6 7 8
Time
a0 = a5 × a0
0x8082
mul a0,a1,a0
a0 = a1 × a0
…
ret
ret
PC = ra
…
…
NOTE: in RISC-V a0/a1/etc are general-purpose registers. ra is “Return Address” register (typically ‘Link Register’ in Arm).

## Slide 19: Pipeline Stalls
Stall:
Pause the pipeline while waiting for availability of resource (e.g., the slow multiply).

## Slide 20: Example: Branch Instruction
int comp(int a, int b){
if (a > b){
return a+b;
} else {
return a-b;
}
}
C (High Level)
ASM (Lower Level)
Binary / Machine
Compiler
Assembler
comp(int, int):
bge a1,a0,16 <.L3>
add a0,a0,a1
ret
.L3:
sub a0,a0,a1
ret
0x00a5d463
0x952e
0x8082
0x8d0d
0x8082

## Slide 21: Pipeline with Branch
  0x00a5d463
  0x952e
  0x8082
  0x8d0d
  0x8082
Storage Media
Fetch
Decode
Execute
0x00a5d463
bge a1,a0,16 <.L3>
PC =.L3 if a1 ≥ a0
0x952e
add a0,a0,a1
0x8082
a0 = a0 + a1
ret
0x8d0d
Clock Cycle: 1 2 3 4
Time
NOTE: in RISC-V a0/a1/etc are general-purpose registers.

## Slide 22: Pipeline with Branch
  0x00a5d463
  0x952e
  0x8082
  0x8d0d
  0x8082
Storage Media
Fetch
Decode
Execute
0x00a5d463
bge a1,a0,16 <.L3>
PC =.L3 if a1 ≥ a0
0x952e
add a0,a0,a1
0x8082
💀
💀
0x8d0d
Clock Cycle: 1 2 3 4 5
Time
NOTE: in RISC-V a0/a1/etc are general-purpose registers.
0x8082
sub a0,a0,a1

## Slide 23: Pipeline Flush
Flush:
Control flow change means pipeline had the wrong instructions – need to throw away the current contents.

## Slide 24: e.g. Typical Specifications – Instruction Latency
https://stnolting.github.io/neorv32/

## Slide 25: Example: A Simple CPU Architecture

## Slide 26: Branch / Pipeline Stall
Q: In previous example – why not just stall pipeline until result is known?
A: Don’t know about the branch until “later” in pipeline.
A: It’s more efficient to just assume branch isn’t taken & keep pipeline up. If branch is random you are right 50% of the time, rather than stalling 100% of the time.

## Slide 27: Branch Prediction
What if we could predict which branches that will be taken? Could get better than 50%! Don’t need time travel even…

## Slide 28: Motivation for Branch Prediction
for(int i = 0; i < datalen; i++){
process_byte(data[i]);
}
loop(char*, int):
addi sp,sp,-16
sw s0,8(sp)
sw s1,4(sp)
sw s2,0(sp)
sw ra,12(sp)
mv s2,a0
mv s1,a1
li s0,0
.L6:
blt s0,s1,.L7
lw ra,12(sp)
lw s0,8(sp)
lw s1,4(sp)
lw s2,0(sp)
addi sp,sp,16
jr ra
.L7:
add a5,s2,s0
lbu a0,0(a5)
addi s0,s0,1
call process_byte(char)
j .L6

## Slide 29: Motivation for Branch Prediction
In this loop example  branch will be taken continuously until only the final iteration. Imagine if datalen = 512, branch not taken 0.195% of time!
The default pipeline behaviour of “assume branch not taken” will have a large (negative) impact on this code-path!
e.g., for NEORV32, adds +3 additional cycles to the loop iteration each time it’s wrong.

## Slide 30: Branch Prediction Example: Pentium
History Bits | Resulting Description | Prediction made | If branch taken | If branch not taken
11 | Strongly Taken | Branch Taken | Remains in same state | Downgraded to weakly taken
10 | Weakly Taken | Branch Taken | Upgraded to strongly taken | Downgraded to weakly not taken
01 | Weakly Not Taken | Branch Not Taken | Upgraded to weakly taken | Downgraded to strongly not taken
00 | Strongly Not Taken | Branch Not Taken | Upgraded to weakly not taken | Remains in same state
https://www.geeksforgeeks.org/branch-prediction-in-pentium/
Branch prediction logic: holds some statement information about latest N seen branch instructions. This state indicates the likely output of the branch:

## Slide 31: Branch Prediction to Speculative Execution
Systems may speculatively execute instructions once we have branch prediction.
Based on predicted branch, load new data into pipeline, and start executing it if something is slow (e.g., waiting on memory).
Need to “unwind” any executed instructions if branch wasn’t taken.
  e.g., can’t start writing to registers yet!

## Slide 32: Out of Order Execution
int ooo(int a, int b, int c){
int e = a * b + 14;
int f = a + b + c;
return e * f;
}
ooo(int, int, int):
mul a5,a0,a1
addi a5,a5,14
add a0,a0,a1
add a0,a0,a2
mul a0,a5,a0
ret

## Slide 33: Out of Order Execution
int ooo(int a, int b, int c){
int e = a * b + 14;
int f = a + b + c;
return e * f;
}
ooo(int, int, int):
mul a5,a0,a1
addi a5,a5,14
add a0,a0,a1
add a0,a0,a2
mul a0,a5,a0
ret

## Slide 34: Out of Order Execution
Execute
a5 = a0 * a1
Clock Cycle: 1 2 3 4 5
Time
a5 = a5 + 14
a0 = a0 + a1
ooo(int, int, int):
mul a5,a0,a1
addi a5,a5,14
add a0,a0,a1
add a0,a0,a2
mul a0,a5,a0
ret
a0 = a0 + a2

## Slide 35: Out of Order Execution
Execute
a5 = a0 * a1
Clock Cycle: 1 2 3 4 5
Time
a5 = a5 + 14
a0 = a0 + a1
ooo(int, int, int):
mul a5,a0,a1
addi a5,a5,14
add a0,a0,a1
add a0,a0,a2
mul a0,a5,a0
ret
a0 = a0 + a2

## Slide 36: Interrupts
Fetch
Decode
Execute
0x00b507b3
add a5,a0,a1
a5 = a0 + a1
0x2a78533
mul a0,a5,a0
0x2a58533
a0 = a5 × a0
mul a0,a1,a0
0x8082
Time

## Slide 37: Cortex-M Pipeline Comparisons
https://en.wikipedia.org/wiki/ARM_Cortex-M

## Slide 38: 6-Stage Pipeline?

## Slide 39: Pipeline Summary
Pipelining is a natural way to improve throughput.
Pipelines are typically 2~5 stages in most microcontrollers you’ll use.
  Stages split between Frontend & Backend
  Frontend: Fetch, Decode
  Backend: Execute, Memory Access, Writeback (Commit)
Pipeline hazards cause a pipeline to stall or require a flush.
Pipelines may feature branch prediction, out of order execution, and speculative execution features to improve throughput.