## Slide 1: Computer Architecture: Performance & Power
Dr. Colin O’Flynn

## Slide 2: Lectures
How does a program run on a machine?
How do you compile from high-level code to machine code?
How does the machine run? (Control Flow)
How does the machine store, access, and control data?
How does the machine execute instructions?
How is execution made more efficient?
How do we measure execution? What is our limit of performance?

## Slide 3: How to measure performance?
Clock speed?
Instructions Per Second?
Instructions Per Cycle?
Power Used?
Something Else?

## Slide 4: Clock Speed

## Slide 5: Instructions Per Second
Rather than pure Hz – measure how many instructions happen in that time.
Slightly better, but no idea what those instructions do.

## Slide 6: Considerations around Performance
We said memory latency can be a driving factor in performance
Consider different workloads:
  Sorting a large dataset
  Calculating a 3D render path
  Calculating the digits of Pi

## Slide 7: What are we trying to benchmark anyway?
Evaluating performance as a user:
  We care about benchmark or results ($ / performance)
Evaluating performance as a developer / engineer:
  We care about our program (instrumenting, etc.)
  This is normally called profiling

## Slide 8: Workload-Based
Most useful benchmarks have some somewhat relatable workload

## Slide 9: Common Benchmarks
Dhrystone:
  Old integer benchmark, not a realistic workload
Whetstone:
  Float-point focused, tries to improve on Dhrystone
EEMBC CoreMark
  Embedded focused – tries to compare various operations you might do on embedded systems (and most common/useful for us)
SPEC CPU
  Desktop/Server CPU evaluation – various more real-life workloads
PassMark CPU Mark
  Commercial benchmark tool – widely used in reviews, evaluations, etc

## Slide 10: Embedded Performance Measurements
How do you select a microcontroller?
Base it on peripherals you need (communication etc), but then what about the code you are running?
  Machine Learning?
  Machine Vision?
  Complex math?
  How much compute is needed?

## Slide 11: CoreMark
Standard embedded benchmark, various “kernels” you can use:
https://www.eembc.org/products/kernels.php

## Slide 12: CoreMark Results
E.g., : https://www.eembc.org/viewer/?benchmark_seq=13489

## Slide 13: Running CoreMark
https://github.com/eembc/coremark

## Slide 14: Measuring Cycles on Embedded Targets
The API at the right uses the Cycle Counter
This is very handy when comparing execution time on embedded systems – most Arm targets support this!

## Slide 15: Power Usage
So far – we’ve considered mostly selecting a processor based on e.g., price, availability, etc.
In real life, what is our limiting factor?
 POWER

## Slide 16: Power Usage vs. Performance

## Slide 17: Dynamic Power Consumption
Switching all those transistors that make up our microcontroller mean switching some capacitance from a logic-0 to a logic-1
General formula for power usage with this is:
Pdynamic = C × V2 × f
  C = capacitance
  V = Voltage
  f = Frequency

## Slide 18: Factors Impacting Power Usage
Capacitance defined by node size
  Newer (smaller) processes have less capacitance as have smaller dies
Voltage has a major (square) impact
  Newer (smaller) often run at lower voltages (5V  3.3V  1.8V  1V)
  Many microcontrollers have a lower core voltage and a higher I/O voltage
Frequency should have a linear impact
  This is one thing you can easily control

## Slide 19: Power Targets
Power (W) = Instantaneous Consumption
Energy (J) = Total consumer over time
Often have some combination of limits of instantaneous power and energy

## Slide 20: e.g., CR2032 Coin Cell
https://data.energizer.com/pdfs/cr2032.pdf

## Slide 21: Simple Battery Power Measurement
235 mAh meaning:
1 mA for 235 hours
100 uA for 2350 hours
10 mA for 23.5 hours

## Slide 22: …kinda

## Slide 23: Other Consideration: Internal Resistance

## Slide 24: e.g., CR2032 @ 125mAh drawn
Open circuit (OC) voltage ~2.8V
Internal Resistance (IR) ~18 ohms
If drawing 50 mA from battery
V = I R = (0.05)(18) = 0.9V
Vload = 2.8 – 0.9 = 1.9V

## Slide 25: Pulse Usage: Capacitor Banks
Common to have a capacitor in parallel with battery to have pulse current capability
This capacitor has a low energy stored however. E.g.:
Assuming 10uF capacitor @ 2.8V
E = ½ × C × V2
= 0.5 × 10E-6 × 2.82
= 39.2 uJ
mAh = Joules / (V × 3.6)
= 0.00000778 mAh
= 0.028008 mAs

## Slide 26: Pulse Usage: Explains common sensor cycles
When designing devices powered from small coin cells (think sensors), you often need to use high-energy / sleep cycles.
Not only for total power saving, but to deal with limited total current.

## Slide 27: Typical Low-Power Modes
Most microcontrollers have some combination of:
Active (normal) mode
Ability to turn on/off peripherals
A low-power mode that keeps everything alive (“sleep” normally)
  SRAM power is ON
A super-low power mode that kills most things (“stop” normally)
  May even turn off SRAM  RAM invalid
Often a mode that leaves a “Real Time Clock” (RTC) Active

## Slide 28: e.g., STM32F3 Clock Gating
Most microcontrollers allow you to turn on/off clocks to peripherals
Many devices have them off by default
This is a common problem if you have a device not working

## Slide 29: e.g., STM32F3 Low-Power Modes

## Slide 30: Always check specifics

## Slide 32: STM32F303: Run Mode vs. Freq

## Slide 33: STM32F303: Sleep Mode vs. Freq

## Slide 34: Stop & Standby Comparison

## Slide 35: CR2032 Battery Callback
Our 235 mAh battery would last:
Mode | Condition | Current (Typ) | CR2032 Life (Ideal)
Run | 72 MHz, Peripherals Disabled | 28 mA | 8.4 hours
Run | 1 MHz, Peripherals Disabled | 1.3 mA | 181 hours / 7.5 days
Sleep | 72 MHz, Peripherals Disabled | 7.0 mA | 34 hours / 1.4 days
Sleep | 0.125 MHz, Peripherals Disabled | 0.8 mA | 294 hours / 12.2 days
Stop | Regulators in run, oscillators off | 21 uA | 1.3 years
Standby | IWDG On | 1.4 uA | 20 years

## Slide 37: Optimizing for Lowest Total Power
Most applications require occasional (at least) wakeup to do something
We could “run fast” == higher power, but more done/second
We could “run slow” == low power, but less done/second
NEVER MAKE ASSUMPTIONS. CHECK FOR DATASHEET DETAILS.

## Slide 38: Optimizing for Lowest Total Power
Also need to consider:
  Time to enter stop mode
  Time to wakeup from stop mode
Graph at right accounts for this & adds power of running for 5000 cycles at different frequencies
https://colab.research.google.com/drive/1sOcllVgW9yIy8QLc2_68LVZ1Cn8YiFNr?usp=sharing

## Slide 39: Optimizing for Lowest Total Power
Graph at right now shows how effect of wakeup/sleep time should be accounted for!
https://colab.research.google.com/drive/1sOcllVgW9yIy8QLc2_68LVZ1Cn8YiFNr?usp=sharing

## Slide 40: Targeting Low Power
Very easy to have a small mistake where low-power doesn’t work. For example from STM32F3 datasheet:

## Slide 41: Common Low-Power Mistakes
Ignore effect of pull-up resistors (10K-ohm resistor @ 3.3V = 330uA!)
Floating inputs
Not shutting down un-needed peripherals (see per-peripheral contribution from datasheet)
Remember datasheet values are often typical, not guaranteed

## Slide 42: Debugging Sleep Problems
Be warned debugging sleep problems is very annoying
  Debugger cannot stay attached during debug (clocks are turned off)
  Need to instrument board carefully to measure low-power
  Have to think about long-term testing & how to accelerate it (if possible)

## Slide 43: Performance & Power Summary
Analyzing performance is not as simple as you might first think!
On embedded systems power is often a bigger driver than performance
We reviewed how to roughly estimate power usage
We demonstrated how to simulate power usage on STM32F3