## Slide 1: Computer Architecture: Layers of Programs
Dr. Colin O’Flynn

## Slide 2: e.g., A Computer Program
#include <stdio.h>
int main(void) {
printf(“Hello World\n”);
return 0;
}

## Slide 4: Considerations Between Layers
Each layer makes assumptions in both directions.
Failing to understand these assumptions & limitations causes:
  Bugs
  Security flaws
  Poor performance (or at least not maximum possible performance)
  Code that doesn’t even work

## Slide 5: SIDEBAR: “Compiler Explorer” (Godbolt.org)

## Slide 6: Example #1 : Blinking an LED (Application)

## Slide 7: Example #1: Blinking an LED (High Level Code)
int gpio_high(void);
int gpio_low(void);
void test(void)
{
while(1){
gpio_high();
_delay_ms(500);
gpio_low();
_delay_ms(500);
}
}

## Slide 8: Example #1: Delays in C on a Microcontroller
int gpio_high(void);
int gpio_low(void);
void test(void)
{
while(1){
gpio_high();
for(int i = 0; i < 5000; i++);
gpio_low();
for(int i = 0; i < 5000; i++);
}
}

## Slide 9: (Backup Slides – Skipped if Live Works)

## Slide 10: (Backup Slides – Skipped if Live Works)
… that is a little easier to understand!

## Slide 11: (Backup Slides – Skipped if Live Works)
... What happened to line 8 on the left !?

## Slide 12: (Backup Slides – Skipped if Live Works)
…Where did the delays go at all?

## Slide 13: (Backup Slides – Skipped if Live Works)
…Where did the delays go at all?

## Slide 14: (Backup Slides – Skipped if Live Works)
This tells the compiler not to touch my variable.

## Slide 15: Example #2: Wait for Button Press
int button_status;
void wait_for_button_press(void)
{
button_status = 0;
while(button_status == 0){
;
}
}
void ISR_PinInterrupt(void)
{
button_status = 1;
}

## Slide 16: Example #2: Global Variable Setting

## Slide 17: Example #2: Global Variable Setting
Line 6 on the right is an infinite loop!
b .L2 means “Branch to Label .L2”

## Slide 18: What was I demonstrating?
The compiler took the High Level Language and made assumptions.
The engineer using the High Level Language didn’t understand what the compiler is going to do.

## Slide 19: Application
This is your design intent. This is the most important step in your design.
We won’t cover this in this course – but this follows from many of your design courses.
Define the problem, constraints, etc.

## Slide 20: High Level Language
This is what most people think of as “programming”
This can be subdivided further – but consider it could mean:
  “Bare Metal” C code
  An RTOS or framework (like FreeRTOS or Arduino)
  Languages like Python or Java which may be interpreted or compiled

## Slide 21: High Level Language
Most Important Embedded Languages (this is purely my opinion)
C: Most common in small embedded systems but used all over.
C++: Common in larger systems, especially Linux based applications.
Java: Now mostly used for Android development. Many embedded systems run Android however.
Rust: A newer memory-safe language, designed to be usable in place of C. Especially popular among Google as developed there (but used extensively outside as well)

## Slide 22: High Level Language
This is the last level at which the code is “machine independent”.

## Slide 23: Intermediate Representation
Compilers have another step that is hidden from us – a language the compiler uses internally for optimizations.
We’ll look at this in more detail in the next lecture.

## Slide 24: Assembly Language
Assembly Language is not machine code.
Assembly Language is human readable code – remember it is further modified by the Assembler.
Assembly language is specific to processors. For example, you may see any of the following:
  Atmel AVR
  Arm
  RISC-V
  x86
  8051 (old but still in wide use)
  MIPS
  PowerPC
  Z80 (very uncommon now)

## Slide 25: Assembly Example:
int check_variable_add(int a, int b){
int c;
if (a == 2){
c = a + b;
} else {
c = a - b;
}
return c;
}
(NOTE: Following slides have static versions – use Godbolt.org and change compiler to see it live)

## Slide 26: ARM

## Slide 27: AVR

## Slide 28: (Another example of Design Intent vs. Compiler)
My choice of “int” has a specific meaning in C. This forces a longer assembly implementation than if I used an 8-bit “char”.

## Slide 29: RISC-V

## Slide 30: x86

## Slide 31: MIPS

## Slide 32: MIPS
MIPS has more fundamentally “out of order” execution. This instruction is always executed.

## Slide 33: PowerPC

## Slide 34: z80

## Slide 35: Machine Code
What the machine sees.
This is the 1’s and 0’s encoded on “something”.
The machine code normally has some relation to how the code is being interpreted or used.
The machine may still make assumptions about things and does not blindly execute.

## Slide 36: e.g., “No Operation” (NOP)

## Slide 37: More Assumptions Compiler/Assembler

## Slide 38: NOP isn’t even used!!!
This does nothing as well (but isn’t the “nop” instruction)

## Slide 39: Arm Machine Code Example
https://vision.gel.ulaval.ca/~jflalonde/cours/1001/h17/docs/arm-instructionset.pdf

## Slide 40: Arm Machine Code Example
https://vision.gel.ulaval.ca/~jflalonde/cours/1001/h17/docs/arm-instructionset.pdf

## Slide 41: Instruction Set Architecture (ISA)
ISA is actually the specification or design document about how the processor works (the diagram at left could combine machine code & ISA).
ISA defines:
  Opcodes
  Registers
  Memory models
  Instruction Encoding
  …etc

## Slide 42: Instruction Set Architecture (ISA)
The ISA is a core part of this course, we’ll be talking about those aspects in great details.
Some ISA specifications are open-source (RISC-V). This does not mean every implementation of them is Open.
Non Open-Source mean you cannot even implement it without some license agreement ($$$).

## Slide 43: Microarchitecture
This defines how the implementation of the ISA is done.
The same ISA may have different implementations (microarchitectures).
Example – your implementation may choose to optimize:
  Low-power (best battery life).
  Lowest cost.
  Highest performance (best speed).

## Slide 44: Example of Trade-Offs
Low-power & low-cost may have similar goals: minimal area (gates).
  Re-use logic as much as possible. Serial calculations that may need to wait for resources to be free.
High-performance
  Task-specific logic, duplicated logic. Use parallel calculations where possible.

## Slide 45: Microcode vs. Hardwired

## Slide 46: Advantages / Disadvantages
Hardwired | Microcode
Implemented with fixed logic – cannot be modified or extended. | Implemented with a microprogram – possible to update this to change/add instructions, sometimes even possible "in the field".
Normally faster due to direct hardware usage. | Normally slower do to microinstruction execution.
Complexity/size can increase substantially as more functions needed. | Complexity/size mostly in software – scales well with large changes or for new functions.

## Slide 47: Logic Gates & Registers
This will be the hardware design itself using gates/flip-flop. Normally defined at the state of "RTL" (Register-Transfer Level).
Examples of RTL are Verilog and VHDL.
Many blocks are still abstractions at this layer – for example memory (SRAM/FLASH) are defined by the foundry.

## Slide 48: RTL Example from neorv32
Open-source RISC-V Processor, see https://github.com/stnolting/neorv32

## Slide 49: e.g., ALU Core
https://github.com/stnolting/neorv32/tree/main/rtl/core
https://github.com/stnolting/neorv32/blob/main/rtl/core/neorv32_cpu_alu.vhd

## Slide 50: RTL Warning / Note
RTL describes hardware – it looks like software but is not. Everything happens concurrently unless otherwise described elsewhere.
I don't plan on diving into RTL in this course unless there is a strong interest in it (Digital Circuits should have introduced it & you'll get more in IC Design if you choose)

## Slide 51: Transistor Level
The output of the RTL tools goes here – if targeting a FPGA will be based on the gate array. If targeting an ASIC requires additional synthesis steps.

## Slide 52: Synthesis Example – 1 bit D Flip-Flop
= 18 transistors total!

## Slide 53: e.g., Discrete Transistor Level
https://monster6502.com/

## Slide 54: Implementation Level
The output of the RTL tools goes here – if targeting a FPGA will be based on the gate array. If targeting an ASIC requires additional synthesis steps.

## Slide 55: Standard Cell Designs
Most foundries provide standard cells – you don't actually synthesize everything to transistor level yourself.
Allows foundry to optimize for specific process.
Blocks could include gates, flip-flops, SRAM, etc. Normally also includes simulation data required to validate your design.

## Slide 56: e.g., D FF Layout
https://www.youtube.com/watch?v=x8lkfS7IFIw

## Slide 57: Implementation Level
Specifics of voltage & process are needed at this stage.
Will define the maximum frequency the device can operate at.

## Slide 58: Gate Width?
https://medium.com/predict/a-node-by-any-other-name-transistor-size-moores-law-b770a16242e5

## Slide 59: Gate Width?
No longer true – note that latest node names are purely marketing.

## Slide 60: Making the Chips

## Slide 62
This course lives here!
IC Design Course
Digital Circuits
Microprocessors