## Slide 1: Computer Architecture: The Debugger & Embedded Systems
Dr. Colin O’Flynn

## Slide 2: Objective of Today’s Lecture
What code did I write?
What code did the compiler generate?
How do we observe it running?
..This will lead into the first lab

## Slide 3: Learning Objectives
What a debugger can and cannot know
Understand how debug symbols map source code to machine code
Observe and understand how optimizations change debugging

## Slide 4: What is a bug?

## Slide 5: What is a debugger?

## Slide 6: Debuggers & Emulators History

## Slide 7: Debuggers: In Circuit Emulators & On-Chip Debug

## Slide 8: Cortex-M In-Circuit Debugger
99% of chips you use will have On-Chip Debug support

## Slide 9: JTAG? SWD?
JTAG is a generic interface for connecting to devices for testing & debug.
A JTAG connection may connect to a debug “core” if the chip has one.
Arm devices may support a “smaller pin count” version of JTAG called Serial Wire Debug (SWD)

## Slide 10: Debugger Connection to System
Debugger
Target System

## Slide 11: Debug Monitors
Monitor Program
Application
Program
Memory
&
Peripherals
$ read_mem 0x2001000, 16
00 00 01 FA FE 0B 0C 0D
AB 02 03 04 1E 00 20 22

## Slide 12: Debug Monitors
Less common now – these existed mainly when on-chip debuggers were not prevalent
The naming remains, we will often see references to a “monitor”
Monitors could break, step code, etc similar to a debugger

## Slide 13: Debuggers & Source Code
What you want to see
What the debugger sees
(Debugger is also missing function names)

## Slide 14: Debuggers & Source Code
What you want to see
What the debugger sees
(Debugger is also missing function names)

## Slide 15: Debug Symbols
Map function names, static variables, etc to addresses:
NOTE: This doesn’t include optimized away variables…

## Slide 16: Debugger Tool #1: Breakpoints
Breakpoints cause execution to “break” (stop)
Control is passed to the debug core / tool at this point

## Slide 17: Code & Data Breakpoints
You set a match on some condition that causes the break
Most commonly we break on a program location (code breakpoint)
You can also break on data read/write ("data breakpoint" or "watchpoint")

## Slide 18: The Program Counter
Will return to this when we talk more about CPU cores, but quickly:

## Slide 19: Assembly vs. C Stepping

## Slide 20: e.g., Many source lines  Fewer Assembly Line

## Slide 21: e.g., One Source Line  Many Assembly Lines

## Slide 22: Register Your Trust

## Slide 23: Simple Loop Example

## Slide 24: Simple Loop Example

## Slide 25: SIDEBAR: Makefile vs. IDE Configuration
Many systems will use a Makefile that has all the compiler options stored in it. You modify the Makefile to change build options (optimization levels etc).
Some Integrated Development Environments (IDEs) allow you to configure this instead – the IDE builds the command based on options you select.

## Slide 26: Simple Loop Example, Again (Optimized)

## Slide 27: Debugger Side Effects
The debugger is pausing your program
The debugger is not pausing the entire world

## Slide 28: Debuggers & Watchdog Timers (WDT)

## Slide 29: Debuggers & Watchdog Timers (WDT)
WDT often have short timeouts (< 100 mS).
If you pause the debugger for longer than that the WDT will reset the system.
You may need to disable the WDT in the source code of your system for debugging.
CAVEATS:
  Some debuggers have an option to automatically detect & do this.
  Some WDT built into microcontrollers have a way to pause during debug

## Slide 30: Debuggers & Interrupts
Interrupts often are time-sensitive – they interface to the outside world
The debugger stops only the core from running – peripherals are often still working (generating interrupts), e.g.:

## Slide 31: e.g., Timer Example
You setup a timer to interrupt every 250 mS
LED Blink Code
Timer
Main Application Code

## Slide 32: e.g., Timer Example
When attemping to step the main code, you will keep hitting the timer interrupt code
WHY: Every 250 mS the timer sets an interrupt flag. At which point the CPU jumps to the interrupt. So you are now continuously debugging the interrupt…

## Slide 33: Debuggers & UART
Similar issues if your device is talking to an external board – the UART interrupt may fire on received data.
You may need to modify your system for debugging!
Some debuggers offer options to:
  Pause timer peripherals
  Automatically allow execution of interrupts

## Slide 34: Debuggers & USB
If you ever need to debug a USB device – this is very annoying, as the device will “time out” from Windows if it stops responding for more than a few seconds!
Need to quickly pause & restart device…

## Slide 35: e.g., Triggering Crashes with Recursion

## Slide 36: Compiler + Debugger Install (Lab Prep)
We are going to use an Integrated Debug Environment (IDE) from Segger in this course:
https://www.segger.com/downloads/embedded-studio/

## Slide 37: Installation Work
Install SEGGER Embedded Studio.
You will be using this academically so can ACCEPT the license agreement (no license needed).
You will need to open the “Package Manager” (it may ask you this the first time) & get a list of packages

## Slide 38: Installation Work (Cont’d)

## Slide 40
1. Search STM32F3
2. Right click on both of these & click "Install"
3. Click "Next"

## Slide 41: Ready for Lab #1
Lab #1 can be done in small groups (1-3 people). Each person will check out a board as you may need to recreate parts of this for the assignment.
We'll explore the debugger usage & see how changes in optimization affect code, as well as understand how to use various debugger features.
The same setup will be used in the remaining labs in the course.