## Slide 1: Computer Architecture: What is a computer?
Dr. Colin O’Flynn

## Slide 2: Solving Problems in History

## Slide 3: ~2100 years ago

## Slide 5: Mechanical, Analog, etc
These computers are built to do a specific task
Sometimes can be reconfigured by changing gears etc, but not a general-purpose computer.

## Slide 6: Turing Complete Machines
A system is Turing complete if it can compute any algorithm, given enough time and memory.

## Slide 7: e.g., NOT Turing complete
A “straight line” machine capable of calculations without branches:
x = a + b;
y = x * 3;
z = y - 1;

## Slide 8: Minimum Viable Turing Machine
State (something that changes)
Conditional behavior
Unbounded repetition
Ability to read/write memory

## Slide 9: Minimum Viable Turing Machine

## Slide 10: e.g., Turing Complete Things
C/C++
Arm Assembly Code
PowerPoint
Excel
The x86 “mov” instruction

## Slide 11: 1st Turing Complete Machine (ish)
The Zuse Z3 (1941)

## Slide 12: Zuse Z3
ISA Summary:
  Two registers (R1, R2)
  Load memory to register
  Arithmetic operation on R1 & R2
  Store R1 & R2 to memory
No conditional branch instruction
  The machine isn’t by design Turing-complete – as a bit of a hack it can be made Turing-complete by running operations to cancel out some.
Despite this – shows early idea of an instruction set

## Slide 13: ENIAC
Designed for artillery firing tables
Online in December 1945
Included a conditional branch – this was the first Turing-complete machine by design in operation.

## Slide 14: Ultimate RISC
It is possible to build a computer with one instruction.
Called One Instruction Set Computer (OISC)
  There is many of them: https://en.wikipedia.org/wiki/One-instruction_set_computer
E.g., FlipJump

## Slide 15: FlipJump
https://esolangs.org/wiki/FlipJump
Opcode: Flips a bit, then jump (unconditionally)
Arguments: a;b
not *a; jump b

## Slide 16: e.g., a FlipJump program
1000;256 // addresses 000-127
32;446 // addresses 128-255
128;256 // addresses 256-383
(Open Excel Example Program)
 Because flipping a bit can change jump, we ultimately get storage, conditional execution, etc

## Slide 17: C to FlipJump Compiler
https://github.com/tomhea/c2fj
Yes you can compile C code to this!

## Slide 18: x86 “mov” instruction
https://github.com/LeetArxiv/ImplementedPapers/blob/main/mov-is-turing-complete.pdf
Comparison of Ri & Rj:

## Slide 19: x86 “mov” instruction as Comparison
Remember – x86 is CISC, so memory-register architecture
If Ri = Rj (e.g., == 123)
Store “0” to address 123
Store “1” to address 123 (overwrite the “0”)
Load address 123 (which now has “1”) to Rk

## Slide 20: x86 “mov” instruction as Comparison
Remember – x86 is CISC, so memory-register architecture
If Ri != Rj (e.g., Ri == 123, Rj == 124)
Store “0” to address 123
Store “1” to address 124
Load address 123 (which has “0”) to Rk

## Slide 21: Turing Completeness?
Having a conditional normally means we can end up with a Turing complete machine.

## Slide 22: PowerPoint as Turing Machine
https://www.youtube.com/watch?v=uNjxe8ShM-8
https://esolangs.org/wiki/(P%E2%84%A2TM%E2%84%A2)%E2%84%A2

## Slide 23: Excel 16-bit Computer
https://github.com/InkboxSoftware/excelCPU
Yes you could be taught this course with only excel.
No this wouldn’t be useful for your career!

## Slide 24: Performance?
None of this talks about performance.
Most work you do in CA is related to making reasonable (useful) performance.
(Almost) anything can compute – but how fast and with how many instructions is where most of our work is.

## Slide 25: e.g.: Early CPU Trainers
https://www.donnamaie.com/AMD_Vintage/AMD_2900_ED2900A.html

## Slide 28: Summary
Turing Complete is the minimum viable requirement for something to execute arbitrary code.
Turing Complete does not mean this is practical or speedy.
Even early processors considered performance – the fundamentals we will cover have been considered since the introduction of the field