## Slide 1: Computer Architecture: Core and ALU
Dr. Colin O’Flynn

## Slide 2: Lectures
How does a program run on a machine?
How do you compile from high-level code to machine code?
How does the machine run? (Control Flow)
How does the machine store, access, and control data?
How does the machine execute instructions?
How is execution made more efficient?
How do we measure execution?

## Slide 3: Tie to ISA Lecture
Several of the topics “should” be call-backs to the ISA lecture
In many instances we are going to look in more detail about why choices where made for the ISA here.

## Slide 4: What’s hidden in here?
We now go inside the magic.

## Slide 5: Arm vs RISC-V
RISC-V is unique as the Instruction Set Architecture is Open Source.
  Other device (such as Arm) have a company behind then – you cannot use the instruction set without paying them $$$.
There are still commercial (closed source) implementations of RISC-V.
But there are also LOTS of open-source processors, simulators, etc.
We can inspect the design of these open-source processors.

## Slide 6: Arm vs RISC-V
In the following slides I’ll switch between RISC-V & Arm cores.
They are very similar for these purposes
Most code examples will use Arm assembly

## Slide 8: Instruction Lifecycle
Fetch instruction
Decode instruction
Read registers
Execute operation
Access memory (if needed)
Write result

## Slide 9: E.g., ADD R1, R2, R3
Fetch E0821003
Decode ADD R1, R2, R3
Read registers
    Operand 1 <= R2
    Operand 2 <= R3
Execute
Result = R2 + R3
Update flags
5. Access memory (not needed)
Writeback
R1 <= Result

## Slide 10: Fetch
Reads data from memory.
May include prefetch buffer of possible instructions (e.g., assume we read next address)
May include issue engine to deal with compressed instructions
https://github.com/stnolting/neorv32/blob/main/rtl/core/neorv32_cpu_frontend.vhd

## Slide 11: Decoding
Example of such decoding was in the 2.0 ISA Slides:
Given 32-bits to encode our instructions, we may invent two simple instruction encoding formats for our processor, e.g.:
Instruction Rd, Rs, Operand2
op | rs1 | rs2 | rd | function
op | rs1 | rs2 / rd | immediate
10
15
20
25
31
0
15

## Slide 12: Decode
https://github.com/stnolting/neorv32/blob/main/rtl/core/neorv32_cpu_control.vhd
Decoding is normally a simple mapping process of bits to various subsystems.
There is a fine line between fetch and decode – typically before any action is taken we consider this the Frontend
Actual work is done in the Backend:

## Slide 13: Register File
Registers are very fast memory near CPU
Discussed in ISA lectures

## Slide 14: Read Registers

## Slide 15: Execute
This is the backend – control (decode) and routing of data to appropriate resource.
Basic operations are actually very simple:
https://github.com/stnolting/neorv32/blob/main/rtl/core/neorv32_cpu_alu.vhd

## Slide 16: ALU
Combination of simple arithmetic operations & flags
Performs comparisons, arithmetic, bitwise operations
https://zipcpu.com/zipcpu/2017/08/11/simple-alu.html

## Slide 17: Status Registers
N = Negative result from ALU
Z = Zero result from ALU
C = ALU operation carry out
V = ALU operation oVerflowed

## Slide 18: Carry Flag
Carry flag is normally set as a result of arithmetic operation:
  SUB
  ADD
Instructions can take the carry as an input:
  ADC (Add with Carry)
  SBC (Subtract With Carry)

## Slide 19: Carry Flag
In Arm specifically:
  On addition, carry flag is set if result > 232 (e.g., overflows unsigned 32-bit)
  On subtraction, carry flag is cleared if a borrow occurs
    This is opposite some architectures, where carry flag is also a borrow flag (set to 1)
Carry flag also used for compare instructions
  CMP = SUB but without a destination (only sets flags)
  E.g:
    CMP R0, #42 => SUB R0, #42
    if R0 == 42:
    Zero flag set (can compare if equal)
    if R0 < 42:
    Carry flag clear (borrow occurred)
    If R0 >= 42:
    Carry flag set (no borrow)

## Slide 20: Arm: Control Flow Reminder

## Slide 21: Overflow Flag
Overflow flag can be thought of “signed carry”
  Remember – sign is using 2’s complement format, where upper bit indicates sign
Set when result of signed operation has opposite sign
e.g., 0x7FFFFFFF = Largest 32-bit signed number possible
0x7FFFFFF + 0x7FFFFFF = 0xFFFFFFFE
Input have sign bit clear
Result does not set carry flag, but does set overflow flag

## Slide 22: Comparisons to 50 years(!) ago

## Slide 26: e.g., Simple Increment with AM2901

## Slide 27: Memory Access
If memory access is “special” (such as load-store architectures) this may be a separate cycle
Perform any load/store to the memory system, not just register access

## Slide 28: Write Back
Output registers are updated
(This is often part of another stage)

## Slide 29: Microprogram Instructions
Even our 50 year old CPU had the idea of microcode or microprogram
Instructions implemented from ALU operations

## Slide 30: Superscalar Processors
Before multi-core processors were popular, we had the idea of superscalar
Allows execution of simultaneous instructions – often duplicating some resources (ALU)
ldr r0, #35
add r2, r3, r4
add r0, r3
add r3, r5

## Slide 31: Superscalar: Different Execution Units (ALU)
https://www.geeksforgeeks.org/computer-organization-architecture/superscalar-architecture/

## Slide 32: Superscalar: Multiple of Same Execution Unit (ALU)

## Slide 33: Instruction & ALU Summary
Instructions are executed in several stages, some of these may be “combined”:
    Fetch instruction
    Decode instruction
    Read registers
    Execute operation
    Access memory (if needed)
    Writeback
Status register flags are an import part of the ALU usage
Microcode-based instructions are a common feature (that may be “hidden” from you)