## Slide 1: Computer Architecture: Memory Busses
Dr. Colin O’Flynn

## Slide 2: Lectures
How does a program run on a machine?
How do you compile from high-level code to machine code?
How does the machine run? (Control Flow)
How does the machine store data?
How does the machine interface using buses?
What does it mean to have “allowed” memory?
How does the machine speed up data access?

## Slide 3
https://web2.qatar.cmu.edu/~mhhammou/15346-s13/resources/OriginsOfComputers/Origins%20Fate%20of%20EDVAC.pdf

## Slide 4: The von Neumann computer

## Slide 5: What is a bus actually?
https://www.madexp.it/2018/02/26/z80-single-board-computer/
(Go to next slide for bigger version)

## Slide 7: Note shared signals:
Address
  Even this simple system has a “memory map” – note use of A15 to select
Data
Some “extra stuff”
Note U3 also on the bus!
ROM
RAM

## Slide 8: Physical Implementation

## Slide 9: Advantages of Buses
Versatility:
  New devices can be added easily
  Peripherals can be moved between computer systems that use the same bus standard
Low Cost:
  A single set of wires is shared in multiple ways
Memory
Processer
I/O Device
I/O Device
I/O Device

## Slide 10: Disadvantages of Buses
It creates a communication bottleneck
  The bandwidth of that bus can limit the maximum I/O throughput
The maximum bus speed is largely limited by:
  The length of the bus
  The number of devices on the bus
  The need to support a range of devices with:
    Widely varying latencies
    Widely varying data transfer rates
Memory
Processer
I/O Device
I/O Device
I/O Device

## Slide 11: Bus Controller vs. Peripheral
A bus transaction includes two parts:
  Issuing the command (and address) – request
  Transferring the data – action
Controller is the one who starts the bus transaction by:
  issuing the command (and address)
Peripheral is the one who responds to the address by:
  Sending data to the controller if the controller ask for data
  Receiving data from the controller if the controller wants to send data
Bus
Controller
Bus
Peripheral
Controller issues command
Data can go either way

## Slide 12: Bus Organization: One Bus
A single bus (the backplane bus) is used for:
  Processor to memory communication
  Communication between I/O devices and memory
Advantages: Simple and low cost
Disadvantages: slow and the bus can become a major bottleneck
Example: IBM PC - AT
Processor
Memory
I/O Devices
Backplane Bus

## Slide 13: Bus Organization: Two Buses
I/O buses tap into the processor-memory bus via bus adaptors:
  Processor-memory bus: mainly for processor-memory traffic
  I/O buses: provide expansion slots for I/O devices
Apple Macintosh-II
  NuBus: Processor, memory, and a few selected I/O devices
  SCCI Bus: the rest of the I/O devices
Processor
Memory
I/O
Bus
Processor Memory Bus
Bus
Adaptor
Bus
Adaptor
Bus
Adaptor
I/O
Bus
I/O
Bus

## Slide 14: Bus Organization: Three Busses
A small number of backplane buses tap into the processor-memory bus
  Processor-memory bus is only used for processor-memory traffic
  I/O buses are connected to the backplane bus
Advantage: loading on the processor bus is greatly reduced
Processor
Memory
Processor Memory Bus
Bus
Adaptor
Bus
Adaptor
Bus
Adaptor
I/O Bus
Backside
Cache bus
I/O Bus
L2 Cache

## Slide 15: e.g., Old Pentium II/III Organization:

## Slide 16: e.g., Newer Gen
More functions now integrated into the main chip.
External busses are always slower…

## Slide 17: Embedded Processor Busses
Busses serve similar purposes even if not external.
Standard bus interface makes it easy to add/remove blocks

## Slide 18: Common On-Chip Bus Protocols
AHB (Advanced High-performance Bus)
  Large bus widths supported, advanced features like bursts
APB (Advanced Peripheral Bus)
  Similar to AHBP but simpler signaling, designed for low-frequency peripherals
AXI (Advanced eXtensible Interface)
  Higher performance than AHB – allows more features like multiple “outstanding transfers”

## Slide 19: Transfer Modes in Busses
Naïve Bus Protocol Implementation (hope data is ready)
Controller
Peripheral
time

## Slide 20: Transfer Modes in Busses
Realistic Bus Protocol Implementation (acknowledge signal)
Controller
Peripheral
time

## Slide 21: Transfer Modes in Busses
Avoiding Stalls: Outstanding Transactions
Controller
Peripheral #1
time
Peripheral #2

## Slide 22: AHB Signaling

## Slide 23: AHB Signals

## Slide 24: Typical Internal Bus Signaling
Not “pin limited”
  Note separate input & output data lines
  Common to have many control signals

## Slide 25: e.g., STM32F3 Bus Matrix

## Slide 26: Bus Arbitration?
A bus may have more than one controller:
  Multi-core processors
  Systems with e.g., a high-performance & low-performance processor
  Special blocks such as DMA
Bus arbitration determines who owns the bus, various algorithms used, but e.g., STM32F3:

## Slide 27: Round Robin
DMA2
Core: I-Bus
DMA1
Core: D-Bus

## Slide 28: DMA
DMA is another bus controller which can read/write from Memory & Peripherals.
Can be triggered by events such as:
  ADC complete
  Packet received (USB, Ethernet, etc)

## Slide 29: DMA Keeps the CPU Free
Examples of common DMA Usage:
  Copy large blocks of data
  Automatically receive incoming data to a buffer
  Take a transmit buffer, read a new “chunk” of data when the peripheral is ready
Large Buffer (>1000 bytes)
USB Packet (64 bytes)
USB Packet (64 bytes)

## Slide 30: DMA Usage
DMA is one of the most powerful features of microcontrollers you can use with high I/O requirements.
Many programs are only possible with DMA, for example:
  USB Microphone would have:
    DMA from ADC Memory
    DMA from Memory  USB
    Microcontroller does “housekeeping” keeping signals alive
Normally required for sampling & high-throughput communications

## Slide 31: e.g., DMA Demo

## Slide 32: Sidenote: Data Synchronization Barrier (DSB)
Note the Data Synchronization Barrier (DSB)
  Technically not needed as peripheral memory should not be reordered
  But if you were writing something to e.g., memory being read from before enabling may still want that (ensures memory consistency)

## Slide 33: DMA Usage: High-Level
Set source & destination addresses
Set if either address should automatically increment (normally not incrementing for peripherals, but do increment for memory)
Set word size (e.g., normally 32 bits)
Set number of words to transfer
  Watch out for Bytes/Words confusion!
Enable & let it go!

## Slide 34: STM32F3 DMA Hints
CPAR / CMAR can be source/dest depending on “DIR” bit in CCR
Watch out that not all memory addresses are accessible (see next topic on TCM/CCM)

## Slide 35: STM32F3: DMA Data Width & Alignments
Many DMA problems (on all devices) are related to data widths.
If not transferring the same data width, need to be very careful about order/alignment.
E.g., Table at right is from ST32F303 Ref Manual

## Slide 36: DMA for Data Packing
Sometimes you use this on purpose:
  8-bit or 16-bit data coming in from a peripheral
  You want this packed into 32-bit array for memory efficiency
    DMA can do that automatically!

## Slide 37: Core Coupled Memory (CCM) Closely Coupled Memory (CCM) Tightly Coupled Memory (TCM)
All of those have the same idea – keep some special RAM that is even faster than system memory.
  Different than a cache as this is separate memory, not mirroring main memory.
  TCM is present in higher-performance cores, may bypass matrix entirely.
  Arm CCM uses matrix, but is not accessible to DMA as only for CPU usage.

## Slide 39: e.g., Cortex-M7 TCM Blocks

## Slide 40: Simple External Busses: SRAM
https://ww1.microchip.com/downloads/en/DeviceDoc/Atmel-6430-32-bit-Cortex-M3-Microcontroller-SAM3U4-SAM3U2-SAM3U1_Datasheet.pdf

## Slide 41: Synchronous Bus
Synchronous buses will have a clock
All data & control signals only read on the clock edge
Normally strict timing requirements
Many internal busses are synchronous (e.g., AHB)
DDR Memory is an external example of synchronous bus

## Slide 42: Asynchronous Bus
Control signals define when data is ready or available
Less strict timing requirements
“Normal” (older) SRAM chips, many “slower” external memories are asynchronous

## Slide 43: Async Read Example
Driven FROM controller
Driven FROM controller
Driven TO controller
Driven TO controller

## Slide 44: Async Write Example
Driven FROM controller
Driven FROM controller
Driven FROM controller
Driven TO controller

## Slide 45: SRAM Configuration

## Slide 46: e.g., Typical SRAM Signals

## Slide 47: SRAM Driven from STM32F3
NOTE: No “acknowledge” signal!
This requires setting up the timing, and the SRAM responds on definite timing.

## Slide 48: Interfacing to External Memory
This requires careful inspection of timing diagrams in your memory chip, comparison to microcontroller datasheet
This is one situation where you should not trust auto-generated code (AI, unknown libraries), as it is often off
Timing errors mean code might work fine initially, but has errors as temperature change

## Slide 49: Example of SRAM (Bus) Timing Settings
https://www.issi.com/WW/pdf/62-65C256AL.pdf

## Slide 50: Bus Wait-States
It is common that busses support wait states
You may need to configure wait states if memory access is slower than the bus is running.

## Slide 51: Busses & Performance
System performance is often limited by bus performance
E.g., processor runs at 72 MHz..but if need 2 wait-states between every FLASH access:
  Naïve reading of flash in sequence slows things down
  Changes to architecture of memory & caches improve that (future topics)
Avoiding wait states can be difficult in practice!
Multiple busses can greatly improve performance.

## Slide 52: Careful Memory Management
e.g., Imagine DMA1 from ADC1 to SRAM
What else can happen at the same time?

## Slide 53: Summary: Memory Busses
Busses are collection of wires, on-chip or off-chip
Typically we have multiple busses with some buffer/interconnect to provide both high & low performance busses, or to avoid needing to wait for other devices.
Split transactions and bus arbitration allow busses to be shared among controllers
Direct Memory Access (DMA) controller is an extremely powerful part of the microcontroller
May need to manage wait-states & timing to deal with different speed interfaces